## Slide 1: Feature Based Design ----------------

## Slide 2: Basics of 3D Modeling
3D models start as 2D Sketches and then they are “Extruded” to become 3D
Once the sketches are extruded (to become 3D) they are know as Parts or Components
2D SKETCH
3D OBJECT (AFTER EXTRUSION)
Adding Material to the sketch (Extruding) is also referred to as “Padding”

## Slide 3: Extruded or Padded Shapes
2D Shape | 3D Object (after extrusion)
Click to add text
Click to add text
Extrusions may be done in any direction and off of any planes or faces

## Slide 4: Feature Based Design
When modeling a simple object it is called a part or component. When more than 1 component or part are attached together it is called an assembly.
3D models often become very complex
There are steps that engineers take to keep their model organized so other engineers not present can still understand it, one is Feature Based Modeling

## Slide 5: Feature Based Modeling
Feature Based Modeling or Parametric Modeling is creating your model based off of features such as:
  Bosses, holes, shafts, fillets, chamfers and pocket
These features are related to each other through constraints, parent-child relationships, and assemblies

## Slide 6: Cont.
This method requires that the model is planned out ahead of time:
  The method of making the model may be planned out (order of operations)
  And calculations to give each sketch proper dimensions and constraints before extruding

## Slide 7: Feature Naming
Designers specify features in engineering terms (pockets, bosses) rather than geometric terms (circles, boxes)

## Slide 8: Example
If one wants to model this part they might decide beforehand to draw it in this order:
    Sketch and extrude base
    Sketch and extrude circular boss
    Cut the hole through the whole part

## Slide 9: Why Feature Based Design?
Can create easily modifiable and accurate models in few steps
Manufacturers and other engineers can see the process you designed the part and all of its dimensions and constraints
Shows step wise process of CADing

## Slide 10: Check Progress
Why is Feature Based Design Important?
What are a few feature names in engineering terms?
What is Feature Based Design?

## Slide 11: Check Progress
Complete supplementary handout to plan steps of each 3D model
Remember to use correct feature names and try to model in fewest number of steps